## Slide 1: Computer Organization and Architecture
Div C SY COMP
Sem III
AY 2024-25

## Slide 2: Computer Organization and Architecture
Course Outcomes
At the end of successful completion of the course the student will be able to
CO 1. Describe and define the structure of a computer with buses
structure and detail working of the arithmetic logic unit and its sub modules
CO 2. Understand the Central processing unit with addressing modes and working of control unit in depth
CO 3. Learn and evaluate memory organization and cache structure
CO 4. Summarize Input output techniques and multiprocessor configurations

## Slide 3: Module 2
Arithmetic and Logic Unit 2.1
Introduction to Arithmetic and Logical unit, Computer Arithmetic: Fixed and Floating point numbers, Signed numbers, Integer Arithmetic, 2’s Complement arithmetic
2.2
Booth’s Recoding and Booth’s algorithm for signed multiplication, Restoring division and non-restoring division algorithms
2.3
IEEE ﬂoating point number representation and operations: Addition. Subtraction, Multiplication and Division. IEEE standards for Floating point representations :Single Precision and Double precision Format

## Slide 4: Introduction to Arithmetic and Logical unit,
Search for ALU diagram
Find which are the signal interface for ALU
Find which are components inside ALU

## Slide 5: Introduction to Arithmetic and Logical unit,
Search for ALU diagram
Find which are the signal interface for ALU
Find which are components inside ALU
Do the calculations
Everything else in the computer is there to service this unit
Handles integers
May handle ﬂoating point (real) numbers
May be separate FPU (maths co-processor)

## Slide 6: Computer Arithmetic
Number System : Binary Numbers
  Fixed Numbers (Unsigned numbers )
    n bit Binary : 0 to 2n -1...total 2n values
    4 bit binary : 0 to 15 ( 24 -1)...total 16 values
  Signed Numbers
    n bit Binary : 2n values, half values negative, half positive MSB reserved for indication of Sign
    0 - positive , 1 - negative
    1’s Complement
    2’s Complement
  Floating Point Numbers
    Short Real
    Long Real

## Slide 7: Signed Number Representation
1’s complement Representation
Complement of binary number ,
0100 1011
sign bit

## Slide 8: Signed Number Representation
1’s complement Representation
Binary Value | Unsigned | Signed 1’s complement
000 | 0 | 0
001 | 1 | 1
010 | 2 | 2
0 1 1 | 3 | 3
100 | 4 | -3
1 01 | 5 | -2
1 10 | 6 | -1
1 1 1 | 7 | -0

## Slide 9: Signed Number Representation
2’s complement Representation
2’s complement = complement of a number + 1
Add 1 to 1’s complement
1011 +1 = 1100
Sign Bit

## Slide 10: Signed Number Representation
Find 2’s complement Representation and its value
  1000
  0100
  111001
  101010
  100000

## Slide 11: Signed Number Representation
2’s complement Representation
Binary | Unsigned | Signed 1’s complement | Signed 2’s complement
000 | 0 | 0 | 0
001 | 1 | 1 | 1
010 | 2 | 2 | 2
0 1 1 | 3 | 3 | 3
100 | 4 | -3 | -4
1 01 | 5 | -2 | -3
1 10 | 6 | -1 | -2
1 1 1 | 7 | -0 | -1

## Slide 12: Signed Number Representation
Signed and Unsigned Numbers
“n” bit number represents 2n values
unsigned numbers are from 0 to 2n - 1
in 2’s complement signed number representation it ranges from -2(n-1) to +2(n-1)-1
for example if n = 4, there are 16 values
Unsigned numbers are from 0 to 15
2’s complement signed numbers are from -8 to +7
What for n= 8? - 2^7 to + 2^7-1
- 128 to 127….256 values

## Slide 13: Floating Point Number Representation
Numbers having integer and fractional part are represented by indicating number in mantissa and exponent form
  32 bit : Short Real Number
  64 bit : Long Real Number

## Slide 14: Integer Arithmetic
Addition and Subtraction
Normal binary addition
Monitor sign bit for overﬂow
Take two’s complement of subtrahend and add to minuend
i.e. a - b = a + (-b)
A | B | Sum | carry | Difference | Borrow
0 | 0 | 0 | 0 | 0 | 0
0 | 1 | 1 | 0 | 1 | 1
1 | 0 | 1 | 0 | 1 | 0
1 | 1 | 0 | 1 | 0 | 0

## Slide 15: Integer Arithmetic
Addition and Subtraction : Unsigned
 | D3 | D2 | D1 | D0
 | 1 | 0 | 0 | 1
 | 0 | 0 | 1 | 1
 | D3 | D2 | D1 | D0
 | 1 | 0 | 0 | 1
 | 0 | 0 | 1 | 1
 | D3 | D2 | D1 | D0
 | 0 | 0 | 0 | 1
 | 1 | 0 | 1 | 1

## Slide 16: Integer Arithmetic

## Slide 17: Integer Arithmetic
Addition and Subtraction : Signed
 | D3 | D2 | D1 | D0
 | 1 | 0 | 0 | 1
 | 0 | 0 | 1 | 1
 | D3 | D2 | D1 | D0
 | 1 | 0 | 0 | 1
 | 0 | 0 | 1 | 1
 | D3 | D2 | D1 | D0
 | 0 | 0 | 0 | 1
 | 1 | 0 | 1 | 1

## Slide 18: 2’s Complement Arithmetic
Subtraction using 2’s Complement 7 - 12
7 = 00111
12 = 01100
-12 = 10100
Since no carry ...it is a negative result , find 2’s complement to get value = 00101 =-5
 | D4 | D3 | D2 | D1 | D0
 | 0 | 0 | 1 | 1 | 1
 | 1 | 0 | 1 | 0 | 0

## Slide 19: 2’s Complement Arithmetic
Subtraction using 2’s Complement 13 - 9
13 = 01101
9 = 01001
-9= 10111
13 - 9 = 13 + ( -9)
Since there is carry ...it is a positive result , = 4
 | D4 | D3 | D2 | D1 | D0
 | 0 | 1 | 1 | 0 | 1
 | 1 | 0 | 1 | 1 | 1

## Slide 20: 2’s Complement Arithmetic

## Slide 21: 2’s Complement Arithmetic

## Slide 22: Integer Multiplication
N X N bit multiplication produces 2N bit result
A | B | Product
0 | 0 | 0
0 | 1 | 0
1 | 0 | 0
1 | 1 | 1
A | B | Product
00 | XX | 00
01 | 01 | 01
01 | 10 | 10
01 | 11 | 11
10 | 01 | 10
10 | 10 | 100
10 | 11 | 110
11 | 01 | 11
11 | 10 | 110
11 | 11 | 1001

## Slide 23: 2 bit Multiplier
 |  | A1 | Ao
 | X | B1 | B0
 |  |  | A0B0
 |  | A1B0 | 
 |  | B1A0 | 
 | A1B1 |  | 
Cy | Cy |  | 
Q3 | Q2 | Q1 | Q0

## Slide 24: Integer Multiplication
Basic 1 Bit Multiplier : AND operation
  AND Gate
Multibit Multiplication
  Array of AND gates and Adders
Propagation of carry : delay incurred
Shift and Add Multiplier
Efficient Arithmetic Circuits: Adder / Multiplier

## Slide 25: Booth Multiplier
Q0 | Q-1 | Action
0 | 0 | Only Shift
1 | 1 | 
0 | 1 | A = A+M, Shift
1 | 0 | A = A-M , Shift

## Slide 26: Booth Multiplier

## Slide 27: Booth Multiplier : 13x 7
A | Q | Q-1 | M | Count | Remarks
00000 | 00111 | 0 | 01101 | 5 | Initial phase
 |  |  |  |  | A<=A-M

## Slide 28: Booth Bit pair Recoding
Multiplier Bit Pair i+1 i |  | Multiplier bit on the right i-1 | Multiplicand selected at position i
0 | 0 | 0 | 0
0 | 0 | 1 | 1
0 | 1 | 0 | 1
0 | 1 | 1 | 2
1 | 0 | 0 | -2
1 | 0 | 1 | -1
1 | 1 | 0 | -1
1 | 1 | 1 | 0

## Slide 29: Booth Bit pair Recoding
13 X -11
Multiplicand 13
Multiplier -11
0 1 1 0 1
1 0 1 0 1
For Booth coding 0 appended and 1 is sign extension for Bit pair coding)
Booth coded Multiplier, Pairs underlined for Bit pair coding
Bit pair coded multiplier
Multiplicand x -1 = 13 x -1 = 1 1 0 0 1 1
0 1 1 0 1
-1_+1 _+1
--------------
0 1 1 0 1
0 1 1 0 1 0 0
1 1 0 0 1 1 0 0 0 0
1 1 0 1 1 1 0 0 0 1
1 1 0 1 0 1 0
0 -1 +1 -1 +1 -1
-1 1 1