## Slide 1
Digital Design Lab
Logic Gates, SOP-POS

## Slide 2
The AND Gate
The OR Gate
The Inverter
The NAND Gate
The NOR Gate
The XOR Gate
The XNOR Gate
NAND as Universal Gate
Gates with More Than Two Inputs
Using Inverters to Convert Gates
TTL & CMOS Logic Gates
Troubleshooting Gate Circuits
IEEE Logic Symbols
Basic Gates

## Slide 3
AND Gate (IC 7408)
OR Gate (IC 7432)
NOT Gate (IC 7404)
EX-OR Gate (IC 7486)
NAND Gate (IC 7400)
NOR Gate (IC 7402)
EX-NOR Gate (EX-OR + NOT Gate)

## Slide 4
“All or Nothing Gate”
Boolean Expression: A · B = Y
Truth Table
The AND Gate

## Slide 6: What is the output of the AND gate?
Unique Output: Output HIGH only when all inputs are HIGH.
?
Low
?
Low
?
?
Low
L
L
H
L
H
H
L
H
TEST
High

## Slide 7
“Any or All Gate”
Boolean Expression: A + B = Y
Truth Table
The OR Gate

## Slide 9: What is the output of the OR gate?
?
?
?
High
High
Low
?
High
Unique Output: Output LOW only when all inputs are LOW.
L
H
H
L
H
H
L
L
TEST

## Slide 10
NOT Circuit
Gives output that is not the same as the input.
Boolean Expression: Y = A or Y = A'
Double inverting: A = A
The Inverter

## Slide 12
NOT AND or inverted AND function.
Boolean Expression: A · B = Y
or (A · B)' = Y
Truth Table
The NAND Gate

## Slide 13: TRUTH TABLE - NAND GATE

## Slide 15: What is the output of the NAND gate?
?
High
?
High
?
Low
?
High
Unique Output: Output LOW only when all inputs are HIGH.
TEST
H
L
L
H
L
L
H
H

## Slide 16
NOT OR or Inverted OR
Boolean Expression: A + B = Y
or (A + B)' = Y
Truth Table
The NOR Gate

## Slide 17
TRUTH TABLE - NOR GATE

## Slide 19
What is the output of the NOR gate?
?
High
?
Low
?
Low
?
Low
Unique Output: Output HIGH when all inputs are LOW.
H
H
L
H
L
L
H
L
TEST

## Slide 20
Known as “Exclusive OR” Gate
“Anything but not all” Gate
Boolean Expression: A  B = Y
Truth Table
The XOR Gate

## Slide 22: What is the output from the XOR gate?
XOR output is HIGH only when odd number of inputs are HIGH
TEST
?
H
H
H
?
H
H
L
?
L
L
H
L
L
L
?
?
Low
High
High
?
Low

## Slide 23
Known as the Exclusive NOR Gate
The Inverted XOR
Boolean Expression: A  B = Y
  or (A  B)' = Y
Truth Table
The XNOR Gate

## Slide 24
TRUTH TABLE - XNOR GATE

## Slide 25
What is the output from this XNOR gate?
L
L
L
?
XNOR output is HIGH only when odd number of inputs are LOW
TEST
?
?
?
H
H
L
L
H
L
H
H
H
Low
Low
High
High

## Slide 26: THE NAND AS A UNIVERSAL GATE
“Universal gate” can be used in combination to create any other logic function.
Example:
A + B
A + B

## Slide 27
USING INVERTERS TO CONVERT GATES
For example:

## Slide 28: PRACTICAL LOGIC GATES
ICs - Integrated circuits
TTL Family of ICs
CMOS (MOS - Metal oxide semiconductor) Family of ICs

## Slide 29: TROUBLESHOOTING SIMPLE GATE CIRCUITS
Logic probe - equipment used to test circuits
Feel top of IC to determine if it is hot
Look for broken connections, signs of excessive heat
Smell for overheating
Check power source
Trace path of logic through circuit

## Slide 30: IEEE LOGIC SYMBOLS
A different set of symbols without unique shapes.
Not very popular at this time.
Examples:
&
A
B
Y
AND gate
OR gate
A
B
Y
1

## Slide 32
NAND as AND
NOR as AND

## Slide 33
NAND as OR
NOR as OR

## Slide 34
NAND as NOT
NOR as NOT

## Slide 35
A.0 = 0 A +1 = 1 | Annulment law
A + 0 = 1 A.1 = A | Identity
A + A = A A.A = A | Idempotent
A + A’ = 1 A.A’ = 0 | Complement Law
((A)’)’=A | Double Negation Law
A + B = B + A A.B = B.A | Commutative Law
A+(B+C) = (A+B)+C A.(B.C) = (A.B).C | Associative Law
A.(B+C) = (A.B)+(A.C) (A+B)(A+C) = A + BC | Distributive Law
Properties of Boolean Algebra

## Slide 36
Canonical and Standard Form
Boolean Function is represented by:
Canonical Disjunctive Normal Form known as minterm
Canonical Conjunctive Normal Form known as maxterm.
Minterm -> functions where the output results in “1”
Maxterm -> functions where the output results in “0”
Sum of minterm - > SOP
Sum of maxterms - > POS
Standard Form – A Boolean variable can be expressed in either true or complementary forms.

## Slide 37
Minterm is expressed in product format and Maxterm is expressed in sum format.

## Slide 38
1. Express the Boolean function F = A + B’C as standard sum of minterms. (canonical SOP form)
Solution –
A = A(B + B’) = AB + AB’
This function is still missing one variable, so
A = AB(C + C’) + AB'(C + C’) = ABC + ABC’+ AB’C + AB’C’
The second term B’C is missing one variable; hence,
B’C = B’C(A + A’) = AB’C + A’B’C
Combining all terms, we have
F = A + B’C = ABC + ABC’ + AB’C + AB’C’ + AB’C + A’B’C
But AB’C appears twice, and according to theorem 1 (x + x = x), it is possible to remove one of those occurrences. Rearranging the minterms in ascending order, we finally obtain
F = A’B’C + AB’C’ + AB’C + ABC’ + ABC
= m1 + m4 + m5 + m6 + m7
SOP is represented as  (1, 4, 5, 6, 7)

## Slide 39
2. Express the Boolean function F = xy + x’z as a product of maxterms (canonical POS form)
Solution –
F = xy + x’z = (xy + x’)(xy + z) = (x + x’)(y + x’)(x + z)(y + z) = (x’ + y)(x + z)(y + z)
x’ + y = x’ + y + zz’ = (x’+ y + z)(x’ + y + z’)
x + z = x + z + yy’ = (x + y + z)(x + y’ + z)
y + z = y + z + xx’ = (x + y + z)(x’ + y + z)
F = (x + y + z)(x + y’ + z)(x’ + y + z)(x’ + y + z’)
= M0*M2*M4*M5 ,
POS is represented as (0, 2, 4, 5)

## Slide 40
3. Convert Boolean expression in standard form SOP F=y’+xz’+xyz
Solution :
F = (x+x’)y'(z+z’)+x(y+y’)z’ +xyz
F = xy’z+ xy’z’+x’y’z+x’y’z’+ xyz’+xy’z’+xyz
4. F(A, B, C) = (1, 4, 5, 6, 7) Find the boolean equation.

## Slide 41
Example: Given the logic equation
Y = (A+BC)(B+ ………………………………..(1)
(a) Simplify in SOP form
Y = A(B+ + BC (B+
Y = AB +A + BC……………….Justify and find minterms
(b) Use NAND Gates only
= . .
c) Simplify in POS form from eqn(1) ….find maxterms
Y = (A+B)(A+C)(B+)(B+A)
d) Use NOR gates only
+ + +

## Slide 42: Karnaugh Maps (K-Maps)
A visual way to simplify logic expressions
It gives the most simplified form of the expression

## Slide 43
Karnaugh Map Representation of Logic Functions: 2 variables, 3 variables, 4 variables
Alternate ways to arrange variables A,B, and C in 3 variables k-map as shown below: Accordingly minterm positions will change.

## Slide 45: Rules to obtain the most simplified expression
Simplification of logic expression using Boolean algebra is awkward because:
  it lacks specific rules to predict the most suitable next step in the simplification process
  it is difficult to determine whether the simplest form has been achieved.
A Karnaugh map is a graphical method used to obtained the most simplified form of an expression in a standard form (Sum-of-Products or Product-of-Sums).
The simplest form of an expression is the one that has the minimum number of terms with the least number of literals (variables) in each term.
By simplifying an expression to the one that uses the minimum number of terms, we ensure that the function will be implemented with the minimum number of gates.
By simplifying an expression to the one that uses the least number of literals for each terms, we ensure that the function will be implemented with gates that have the minimum number of inputs.

## Slide 46: Three-Variable K-Maps

## Slide 47: Three-Variable K-Map Examples

## Slide 48: Four-Variable K-Maps

## Slide 49: Four-Variable K-Maps

## Slide 50: Four-Variable K-Maps Examples

## Slide 51: Four-Variable K-Maps Examples

## Slide 52: Four-Variable K-Maps Examples

## Slide 53: Design of combinational digital circuits
Steps to design a combinational digital circuit:
  From the problem statement derive the truth table
  From the truth table derive the unsimplified logic expression
  Simplify the logic expression
  From the simplified expression draw the logic circuit
Example: Design a 3-input (A,B,C) digital circuit that will give at its output (X) a logic 1 only if the binary number formed at the input has more ones than zeros.

## Slide 54: Design of combinational digital circuits (Cont.)
Example: Design a 4-input (A,B,C,D) digital circuit that will give at its output (X) a logic 1 only if the binary number formed at the input is between 2 and 9 (including).

## Slide 55: Design of combinational digital circuits (Example)
Example: Design a 4-input (A,B,C,D) digital circuit that will give at its output (X) a logic 1 only if there more ones than zeros in the binary number formed at the input.